## Slide 1
GeoReach
Geospatial Accessibility Intelligence for Flood Response
Which villages get cut off when Assam floods — and who to reach first.
WHY IT MATTERS
Every monsoon, the Brahmaputra severs road links between remote settlements and the hospitals that serve them. Relief teams lack a fast, evidence-based map of which places are isolated — and where to send boats first.
FOCUS AREA
Dhemaji
Lakhimpur
Majuli — world's largest river island
75+
lives lost
700K
people displaced
900+
villages submerged
Assam floods, 2026

## Slide 2
Engineering Workflow
A reproducible pipeline from raw open data to a decision-ready map — end to end in ~23 seconds.
1
Acquire
OpenStreetMap roads, hospitals, bridges & district boundaries; Census 2011 populations
>
2
Map the flood
Sentinel-1 SAR change detection in Earth Engine; permanent water removed to isolate NEW flooding
>
3
Build network
9,090 road segments to a junction-aware graph (connectivity fixed: 27,000 to 144 fragments)
>
4
Assess access
Multi-source Dijkstra from every hospital to each village; DEM-derived flood depth
>
5
Prioritise
Weighted score: access loss, population, infrastructure, isolation, depth to ranked triage
BUILT ENTIRELY ON OPEN / PUBLIC DATA
Sentinel-1 SAR
SRTM DEM
OpenStreetMap
Census 2011
CWC gauges
ASDMA reports
Python · GeoPandas · NetworkX · rasterio · Folium/Leaflet

## Slide 3
Results — Observed 2026 Flood
Driven by real Sentinel-1 satellite flood extent over the three districts.
22%
of roads cut off
2,013 of 9,090 segments
49
settlements isolated
6 critically isolated
807 km²
area flooded
depth 0.2 - 12 m (SRTM)
Chart: 
| Accessible | Isolated | Critically isolated | Partial
Accessibility | 29 | 43 | 6 | 2
80
villages
Accessible 29
Isolated 43
Critically isolated 6
Partial 2
TOP PRIORITY TO REACH FIRST
1
Jonai
pop 15,420 · critically isolated
2
Gogamukh
pop 12,750 · critically isolated
3
Dhakuakhana
pop 12,800 · critically isolated
4
Kamalabari
pop 12,200 · critically isolated
5
Bihpuria
pop 10,500 · critically isolated

## Slide 4
Innovation & Impact
S
Real satellite flood
Sentinel-1 SAR sees through monsoon cloud; permanent-water exclusion isolates genuinely new inundation
E
Terrain-derived depth
Flood depth computed from SRTM elevation inside each flooded area — not a flat assumption
N
Junction-aware routing
Rebuilt the road graph so intersections connect (27,000 to 144 fragments), making isolation real
T
Multi-criteria triage
Transparent weighted scoring turns raw geography into a ranked, defensible action list
IMPACT
Turns days of manual assessment into a 23-second, repeatable run. Gives disaster authorities an interactive map of who is cut off and where to send boats first — transferable to any flood-prone district, built entirely on free, public data.